## Slide 1: Rethinking Resource Concerns
Version 1.5.02 – 2017-07-26
(ESD Draft Working Version)

## Slide 2: Contents
Goal and Concepts
Fundamentals of Systems
Land-Unit Systems
Natural Resources, Events, and Features
Land Uses, Activities, and Features
Resource Concerns
Planning Criteria and Assessment

## Slide 3: Goal
The goal of the effort is to establish an overarching, science-based, framework for the resource concern basis underpinning NRCS’ conservation work that will enable NRCS to meet the many challenges facing agricultural conservation in the next 25 years.

## Slide 4: Concepts for the Framework
Provides an overarching framework for the natural resources basis underpinning conservation;
Is science-based and founded upon first principles;
Uses system theory and concepts to organize landscapes, natural resources, and land uses into internally-consistent, coherent, organized systems;
Represents these systems using conceptual models (system models) that represents system structure, components, processes, and flows;
Uses simple, plain English, not human-value laden terminology that is readily understood by the field, producers, partners, and the public;
To the extent possible, retains existing NRCS constructs and terminology and minimizes institutional change; and
Provide a decision-tree output to accelerate the planning assessment process and simplify the incorporation of this concept into computerized systems.

## Slide 5: Fundamentals of Systems
(aka Systems 101)

## Slide 6: System Fundamentals
System boundary
Components (fixed and movable):
  Matter, material things
  Energy, in various forms
  Other: Information, money, etc.
Processes: transformations, movements, storage/release, etc.
Inputs and outputs (open system)
Systems within systems (subsystems)
System types: natural, human-constructed, and mixed

## Slide 7: System #1
System – an interacting or interdependent set of things so related or connected as to form a unified whole
System Boundary (Open System)
Inputs
Process
Outside the System
Outputs
System
Components
Fixed
Mobile

## Slide 8: System #2
Matter
Matter
Energy
Energy
Matter
Matter
System Boundary
Process
Energy
Matter
Matter
Legend
Energy

## Slide 9: Subsystems
Systems within systems
Subsystem
(Open)
Subsystem
(Open)
System
(Closed)
Subsystem
(Open)

## Slide 10: Natural, Human, and Mixed Systems
Natural Systems
  Outcome of natural processes: self-designing
  May have “fuzzy” system boundary
  No purpose or objective
Human-Constructed Systems
  Human-designed and built
  Usually have a well-defined boundary
  Built for a purpose/use (e.g., production)
  Has associated costs (land, labor, capital)
Mixed Natural/Human Systems

## Slide 11: Land-Unit Systems

## Slide 12: Land-Unit Systems
 | Land-Unit Scale | Natural | Human (Use, Planning, Production)
Onsite | Site | Ecological Site | Use: Management, Production, Cultural, Planning Land Unit (PLU), Common Land Unit (CLU)
Offsite | Local | Ecological System (Ecosystem) | Farm, Operation, Conservation Management Unit (CMU)
 | Regional | Ecoregion, Watershed | County, State, MLRA, Area, Region
 | Global | World | World
Ecoregion
World
Ecosystem
E. Site
Area
CMU
CLU
Not to Scale

## Slide 13: Ecological System/Sites with Natural Resources
Air
Soil
Native Vegetation Cover (Plants)
Land
Ground Water
Minerals
Seeds
Precipitation
Animals
Surface Water
Sed-Chem
Runoff
Sediment (Dust)
Solar Energy
Wind Energy
Heat Energy
Animals
Evapotranspiration
Ecosystem Boundary
Ecological
Site
Ecological
Site
Ecological
Site
Ecosystem
Processes

## Slide 14: Site-Offsite Effects
World
Ecoregion
Site
Ecosystem
Site Effects
Decreasing
Offsite Effects
Decreasing

## Slide 15: Production Systems

## Slide 16: Production System (Factory) Site
Raw Materials
Products - Goods
Infrastructure
Liquid/Gas/Solid Fuels,
Electricity, Labor
Delivered Water
Contaminants
Energy
Waste Energy
Equipment
Machinery

Waste Byproducts
Waterborne,
Solid, Airborne
Production System (Site) Boundary
Infrastructure
Production
Processes
Notes: A production system, at its most basic level, is one or more transformation processes (i.e., production processes) that transform resources into useful goods, products, or services.
Production resources are commonly called by economists the “factors of production” and include labor, capital (machinery, equipment, and materials), and production space (land and buildings).
A production system may be characterized by “flows” or movement of raw materials to finished products.

## Slide 17: Production System Cost Flow
Raw Materials
Products - Goods
Infrastructure
Liquid/Gas/Solid Fuels,
Electricity, Labor
Delivered Water
Contaminants
Energy
Waste Energy
Machinery
Equipment

Waste Byproducts
Waterborne,
Solid, Airborne
$
$
$
$
$
$
$
$
$
Production System (Site) Boundary
Production
Processes

## Slide 18: Ecological System & Crop Production System/Site
Land
Ground Water
Minerals
Seed, Fertilizer, Pesticides
Food/Fiber
Pests
Waste Energy
Tillage

Heat Energy
Solar Energy
Energy (Fuel)
Soil
Planter
Pest Equip.
Precipitation
Harvester
Fertilizer
Growth
Sediment (Dust)
Sediment
Runoff
Chem Waste
Delivered Water
Crop
Native Vegetation Cover (Plants)
Soil
Evapotranspiration
Ecosystem
Processes
Production
Processes
?

## Slide 19: Ecological System and Production System (Factory) Site
Soil
Vegetation Cover (Plants)
Land
Ground Water
Minerals
Raw Materials
Products
Infrastructure
Machinery
Delivered Water
Contaminants
Energy
Waste Energy
Equipment

Waste Products

## Slide 20: Natural Resources, Events, and Features

## Slide 21: Resource Definitions
Natural Resource: Any naturally occurring resource needed by an organism, population, or ecological system. NRCS applies this term to soil, water, air, plants, animals, energy, and humans (SWAPAE+H). (Current NRCS definition)
Resource: Something that is used by or benefits an organism or system.
Natural Resource: A resource in a form and state as it occurs in nature.

## Slide 22: Natural Resources
  Material Resources
    Abiotic (Non-living)
      Minerals
      Soil
      Water
        Precipitation
        Surface water
        Ground water
      Air
    Biotic (Living)
      Plants
      Animals
      Other
  Energy Resources
  Solar
  Wind
  Hydropower
  Geothermal
  Space Resources
    Land
    Water
    Air

## Slide 23: Human Products from Natural Resources
  Material Resources
    Abiotic (Non-living)
      Steel
      Concrete
      Potting mix
      Bottled or piped water
    Biotic (Living)
      Cultivated crops
      Livestock
      Domesticated animals
  Energy Resources
  Electricity
  Gasoline and diesel fuel
  Space Resources
    Built lands
    Reservoir
+ many others

## Slide 24: Two Types of Resource Characteristics
Quantity Characteristic
  Magnitude or multitude
  Amount: number, area, volume, weight, other
  Rate: amount per time
  Density: amount per area
  Amount change (+/-)
  Time of occurrence
Quality Characteristic
  Presence/concentration of component
  Presence/concentration of impurity
  Density/intensity/purity
  Diversity/composition
Note: Quantity and Quality characteristics do not imply quantitative and qualitative measurements.

## Slide 25: Natural Resources/Characteristics
Soil
  Soil Quantity
  Soil Quality
Water
  Water Quantity
  Water Quality
Air
  Water Quantity
  Water Quality
Plants
  Plant Quantity
  Plant Quality
Animals
  Animal Quantity
  Animal Quality
Energy
  Energy Quantity
  Energy Quality
Land
  Land Quantity
  Land Quality

## Slide 26: Space Resources
Spaces (places): land surface, water surface, air space, underground space, below water surface
Space (place) where natural and human-build features are located and events and activities occur
Type conversion
  Land to water (reservoir)
  Water to land (diked and drained sea)
Land reconfigurations
  Leveling
  Terracing
  Raising/lowering through material import/export

## Slide 27: Animals and Plants: Resources Using Resources
Animals
Soil
Water
Air
Solar
Energy
Plants
Space
Land, air, water
Photosynthetic energy
CO2
N, K, P, others
Place to Grow
H2O
H2O
O2
Place to live, territory
Food (nutrients)
Food (nutrients)
Humans
Pollination, seed dispersal, etc.

## Slide 28: Natural Resource Renewability
Perpetual: Availability is independent from human uses
  Solar energy, wind energy
Renewable: Can last into perpetuity if properly used and managed
  Trees, streamflow, animals
Non-renewable: Finite in quantity, not renewed by natural processes (within a human time frame*), and therefore can be depleted
  Minerals, soil, some ground water
*Within a human/management time frame; < 100 years

## Slide 29: Natural Resource Relationship to Site
Fixed: Can not be removed from site
  Solar energy, precipitation
Movable/Removable: Possible to move from or be removed from site
  Minerals, soil, trees
Mobile: Can readily move on and off a site
  Flowing surface water, animals

## Slide 30: Natural Events
Natural Event: An instance of a natural process(es) not resulting from human land uses, activities, or built features. Examples include soil formation, rainfall events, runoff events, river channel shifts in location, wildfires, landslides, and animal migrations. Natural events can trigger other events in cascades of events. Natural events can (sometimes) be modified by human land uses, activities, and built features.
Rainfall
Event
Runoff
Event
Soil
Erosion
Event
Example:
Streamflow
Sediment
Transport
Sediment
Deposition

## Slide 31: Natural Event Temporal Metrics
Event Frequency*
Rare (<1% of years)
Infrequent (<20% of years)
Frequent (>20% of years)
Annual occurrence
Multiple times per year
Continuous
Event Effect Longevity*
Temporary
Short-term (<1 year)
Long-term (>1 year)
Permanent
*Within a human/management time frame; < 100 years
Event Duration*
Instantaneous
Short-term (<1 year)
Long-term (>1 year)
In perpetuity

## Slide 32: Land Uses, Activities, and Features

## Slide 33: Land Use, Activities, Features
Land Use: A set of related activities, features, and inputs on a land unit used for a purpose, such as providing a product or service, and usually—but not always—related to a land cover type.
Activity: Actions by humans—or other animals—seeking a particular outcome.
Built Feature: A non-natural landscape feature, including reshaped land, infrastructure, buildings, facilities, and vegetation cover resulting from a human activity.
Land Unit
Land Use
Feature
Activity 3
Activity 4
Activity #
Activity 1
(One Time)
Feature
Product
or Service*
*Including ecosystem services
Delivered Inputs
Activity 2
(Multiple Times)

## Slide 34: Road (Developed Land Use) Example
Road Corridor Site
Developed Land
O&M
Striping, salting, sanding, pothole filling
Vehicle transit
Road Construction
Roadway
Transport of People and Goods
Asphalt, Paint, Salt, Sand, Signs, etc.

## Slide 35: Crop Production Example
Crop Production
Land Use
Tilling
Site
Development
Farm
Field
Food, Fiber, or Fuels
Seed, Fertilizer, Pesticides,
Crop Cover
Fertilization
Pest Control
Harvesting
Planting

## Slide 36: Terminology: Natural and Human
Natural | Human
Land Cover Land Use | Land Cover Land Use
Natural Resource | Human Product
Event | Activity
Landscape Feature | Built Feature

## Slide 37: Land Uses
Crop production
Forest-related product production
Grazed land-livestock production
Confined animal facility-livestock production
Mineral resource extraction
Water management
Waste management
Infrastructure, building, facility, or utility site/corridor use
Wildlife use
Recreation use
Military/government use
Conservation, protection, and unmanaged land uses

## Slide 38: Land Use Activities and Features
Example for Crop Production, Forest Product Production

## Slide 39: Human Activity Temporal Metrics
Activity Frequency*
Once
Infrequent (<2% of years)
Occasional (<=10% of years)
Frequent (>10% of years)
Annual occurrence
Multiple times per year
Continuous
Activity Effect Longevity*
Temporary
Short-term (<1 year)
Long-term (>1 year)
Very long-term (>100 yr)
Permanent
Activity Duration*
Instantaneous
~Day
Short-term (<1 year)
Long-term (>1 year)
In perpetuity
*Within a human/management time frame; < 100 years

## Slide 40: Multiple Land Uses on a Site
A site (or larger land unit) may have multiple land uses. These uses can be:
  Sequential: One land use is completed and another begins.
  Simultaneous: Two or more land uses occur at the same time.
Mineral
Extraction
Sequential
Simultaneous
Simultaneous
Wildlife
Recreation
Crop
Production
Wildlife
Unmanaged
Wildlife

## Slide 41: Effects of Land Uses (Human Activities, Built Features, and Delivered Inputs) Upon a Natural Resource
Increase/decrease resource quantity
Change a resource quality
No Effect
Not Applicable

## Slide 42: Resource Concerns

## Slide 44: NRCS Resource Definitions
Resource Concern: An expected degradation of the soil, water, air, plant, or animal resource base to the extent that the sustainability or intended use of the resource is impaired. (NPPH)
Resource Problem: The resource condition that does not meet the minimum acceptable condition levels as established by resource planning criteria shown in the FOTG, Section III. (NPPH)

## Slide 45: Current NRCS Resource Terminology
Resource Terms
Examples
Soil
  Soil Erosion
    Concentrated Flow Erosion
      Ephemeral Gully Erosion
      Classic Gully Erosion
Water
  Water Quality Degradation
    Excess Nutrients in Surface Water and Groundwater
      Excess Nutrients in Surface Water
      Excess Nutrients in Groundwater
Screening/Assessment
Natural Resource
  Resource Consideration/Concern
    Resource Concern Cause
      Resource Concern Component
      Micro-Resource Concern
      CSP: Resource Concern Cause?

## Slide 46: Current NRCS Natural Resources Considerations/Concerns
Soil
  Soil Erosion
  Soil Quality Degradation
Water
  Excess/Insufficient Water
  Water Quality Degradation
Air
  Air Quality Impacts
Plants
  Degraded Plant Condition
Animals
  Inadequate Habitat for Fish and Wildlife
  Livestock Production Limitation
Energy
  Inefficient Energy Use

## Slide 47: Land-Unit/Resource Relationships
USE SITE
Natural Resources
Land-Use Activities
Human-Built Features
Human Delivered Inputs
Human Produced Outputs
ECOSYSTEM
Natural Resource Inputs
ECOSYSTEM
Natural Resource
Outputs
WORLD
WORLD
ECOREGION
ECOREGION

## Slide 48: Concern Type Based Upon Land Use—Natural Resource Relationships
Natural Resource
Land Use
affects
Natural Resource
Land Use
affects
A resource concern arises from a disparity or incongruity between a required natural resource condition and land use objectives, activities, or built features.

## Slide 49: Five Resource Concern Types
1. Use Limitation Concern
2. Use Sustainability Concern
5. Ecosystem Sustainability Concern
3. Use Hazard Concern
4. Ecosystem Concern

## Slide 50: 1. Use Limitation Concern
The quantity of a natural resource available on a site limits a desired land use, or
The quality of a natural resource available on a site limits a desired land use.
Examples:
Precipitation amount received limits crop production
Soil salinity limits crop productivity
Low forage quality limits livestock stocking rate
SITE
Natural Resource
SITE
Land Use
limits
Use Limitation Concern: Quantity or quality of an onsite natural resource is or will be a limiting factor for a desired land use.

## Slide 51: 2. Use Sustainability Concern
SITE
Land Use
SITE
Natural Resource
affects
limits
Example:
Soil erosion rate in excess of T will deplete the site soil resource and limit future crop production
Use Sustainability Concern: Quantity or quality of an onsite natural resource is being depleted/degraded at a rate such that it may be unavailable for future use.
Natural resource depletion rate will limit future natural resource availability, or
Natural resource quality changes will limit future natural resource availability.

## Slide 52: 3. Use Hazard Concern
The quantity of a natural resource poses a hazard, or
The quality of a natural resource poses a hazard.
ECOSYSTEM
Natural Resource
SITE
Land Use
is hazardous to
Examples:
A high flood hazard poses a risk to buildings on the site
High wildfire potential poses a hazard to livestock and buildings
Karst geology poses a building and land use activities hazard
Hazard Concern: Quantity or quality of a natural resource creates a potential hazard to people, animals, infrastructure, and facilities.

## Slide 53: 4. Ecosystem Concern
Site land use increases (or decreases) natural resource quantity in the surrounding ecosystem, or
Site land use changes natural resource quality in the surrounding ecosystem.
SITE
Land Use
ECOSYSTEM
Natural Resource
affects
Examples:
Urban paving increases runoff and downstream flood discharge
Applied fertilizer not incorporated into crop increases surface water nitrate levels
Site land use fragments a wildlife corridor
Ecosystem Concern: Land use is such that quantity or quality of a natural resource is being changed and such change may potentially degrade environmental conditions, create hazards, or limit uses (applies both to onsite effects and offsite ecosystem effects).

## Slide 54: 5. Ecosystem Sustainability Concern
Natural resource depletion rate will limit future natural resource availability, or
Natural resource quality changes will limit future natural resource availability.
Example:
Groundwater withdrawal rates higher than recharge rates will deplete aquifer groundwater reserves
SITE
Land Use
ECOSYSTEM
Natural Resource
affects
limits
ECOSYSTEM
Land Uses(s)
affects
limits
Ecosystem Sustainability Concern: If a natural resource is being depleted or degraded at a rate such that it may be unavailable for future use, it becomes a sustainability concern.

## Slide 55: Issue/Concern/Problem Statements
[Adjective] [Resource] [Quantity or Quality] [Limits/Is hazardous to] [Land Use]
[Land Use] Causes [Resource] [Quantity or Quality] [Noun]
Adjectives
Insufficient (quantity) – not enough
Excessive (quantity) – too much
Inadequate (quality) – unsatisfactory
Hazardous (quantity, quality) – hazardous
Nouns
Depletion (quantity) – resource being diminished
Excess Generation (quantity) – resource being increased
Degradation (quality) – resource quality being lowered
Site Concerns
Ecosystem Concerns

## Slide 56: Resource Concern Relationship to Resource Use/Hazard or to the Ecosystem
Use/Hazard Concerns
  Insufficient—not enough of an onsite natural resource is available for desired land use
  Excessive—too much of a natural resource onsite limits desired land use
  Inadequate—natural resource quality is unsatisfactory for desired land use
  Hazardous (quantity)—extreme amount of resource onsite poses a hazard to life and/or property
  Hazardous (quality)—natural resource quality poses a hazard to life and/or property
Ecosystem Concerns
  Depletion—land use partially to fully reduces the quantity of an onsite and/or ecosystem natural resource
  Excess Generation—land use increases the quantity of an ecosystem natural resource to an excessive magnitude
  Degradation—land use reduces the quality of a site and/or ecosystem natural resource

## Slide 57: List of Resource Concerns
Soil
Soil Quantity
  Insufficient
  Depletion
Soil Quality
  Inadequate
  Degradation
Water
Water Quantity
  Insufficient
  Excessive
  Hazardous
  Depletion
  Excess Generation
Water Quality
  Inadequate
  Hazardous
  Degradation
Air
Air Quality
  Inadequate
  Degradation
Plants
Plant Quantity
  Insufficient
  Excessive
  Hazardous
  Depletion
Plant Quality
  Inadequate
  Hazardous
Animals
Animal Quantity
  Insufficient
  Excessive
  Depletion
  Excess Generation
Animal Quality
  Hazardous
Energy
Energy Quantity
  Insufficient
Land
Land Quantity
  Depletion
Land Quality
  Inadequate
  Hazardous

## Slide 58: Resource Concern Causes: Soil
Insufficient Soil Quantity
  Insufficient onsite soil depth for crop production and forest product production
Soil Quantity Depletion
  Soil depletion resulting from accelerated erosion above natural geologic rates limits future land use of the site
  Soil depletion due to land use (e.g., mineral extraction) limits future land use of the site
Inadequate Soil Quality
  Inadequate soil quality limits crop, tree, or forage productivity on the site
  Inadequate soil quality for infrastructure or facility construction on the site
Soil Quality Degradation
  Soil quality degradation results from intensive land use and potentially limits future land uses on the site

## Slide 59: Resource Concern Causes: Water
Insufficient Water Quantity
  Insufficient onsite water limits crop, tree, or forage production
  Insufficient or poor distribution of water limits livestock production goals
Excessive Water Quantity
  Excessive water limits crop, tree, or forage production
  Excessive water limits infrastructure and facility construction
Hazardous Water Quantity
  Flood flows make land use hazardous for humans, livestock, and structures
Water Quantity Depletion
  Water depletion due to withdrawals from a stream/river decrease downstream flows and degraded ecosystem conditions
  Water depletion due to withdrawals from a groundwater aquifer cause aquifer depletion and potential aquifer loss
Excess Water Quantity Generation
  Excess water generation due to land use increases downstream flooding
Inadequate Water Quality
  Inadequate water quality for desired use due to high concentrations of pollutants
Hazardous Water Quality
  Water quality is hazardous to humans or animals
Water Quality Degradation
  Surface water quality is degraded by land use pollutant runoff
  Surface water quality condition (e.g., temperature) is degraded by land use

## Slide 60: Crop Production Example Non-Irrigated
Soil quantity
  Insufficient
  Depletion
Soil quality
  Inadequate
  Degradation
Water quantity
  Insufficient
  Excessive
Water quality
  Degradation
Air Quality
  Inadequate
  Degradation
Plant quantity
  Excessive
  Depletion
Animal quantity
  Excessive
  Depletion
Land quality
  Inadequate
  Hazardous
[Adjective] [Resource] [Quantity or Quality] [Limits/Is hazardous to] [Crop Production]
[Crop Production] Causes [Resource] [Quantity or Quality] [Noun]

## Slide 61: Livestock Production Example
Water quantity
  Insufficient
  Hazardous
Water quality
  Inadequate
  Degradation
Plant quantity
  Insufficient
  Hazardous
Plant quality
  Inadequate
  Degradation
  Hazardous
Animal quantity
  Excessive (pests)
Land quality
  Hazardous
[Adjective] [Resource] [Quantity or Quality] [Limits/Is hazardous to] [Livestock Production]
[Livestock Production] Causes [Resource] [Quantity or Quality] [Noun]

## Slide 62: “Suites” of Characteristics
A set of resource characteristics necessary to meet a land use requirement.
  Drinking water quality (human/animal)
  Recreation water quality (recreation)
  Soil health (crop production)
  Building site suitability (developed land uses)

## Slide 63: Causes for Resource Concern: Water Quality Example
Inadequate water quality
  High sediment concentration/turbidity
  High salt/TDS
  High nutrient concentration
  High metal(s) concentration(s)
  High toxin concentrations
  High pathogen concentrations
  High temperature
  Low dissolved oxygen

## Slide 64: Resource Concern Filter
LAND UNIT
Natural Resource Characteristics
A resource concern filter is the means used to compare a set of quantity and quality natural resource characteristics with established criteria to determine whether or not there is a resource concern associated with a land use or its objectives, land-use activities, or built features.
Resource Concern Filter
CRITERIA
Resource Concern Type
LAND USE
Objectives
Activities
Built Features
Resource Concern
Y or N

## Slide 65: Primary Steps in the Filter
Identify land use (O-A-F)
  Objectives (client use objectives)
  Activities
  Features
Identify land unit resource characteristics pertinent to land use
For each resource concern filter, compare land use O-A-F to land unit resources
  Comparison to criteria: Y/N for resource concern

## Slide 66: Filter Intensification
Does O-A-F occur on not occur?
  First filter-occurs: Y/N
  How intensive/extensive is the activity?
How significant is land unit resource condition(s) to the O-A-F?
  Resource impact: Low-Med-High
  Second filter-significance: activity intensity/resource significance matrix
How does O-A-F compare with established criteria?
  Tool used to provide comparison to criterion

## Slide 67: Planning Criteria
Assessment: The act of assessing the physical condition or extent of management applied.
Planning Criteria (PC): Criteria established for natural resource quantity and quality characteristics used to determine whether or not there is a resource concern associated with a specified land use–its objectives, land-use activities, or built features. Planning criteria may be based upon resource limitation for a specified use, natural resource hazard potential or risk, or environmental concerns within the ecosystem.
Screening: Use of available information to identify sites with conditions that have little or no probability of needing additional treatment to address the specific resource concern. Screening may utilize available soils data, management information from the farmer, visual observations, and/or site conditions.

## Slide 68: Resource Concern Decision-Tree Approach
A decision-tree approach that replaces the existing resources concerns and planning criteria tabular approach is used to help guide the planner through the assessment process to simplify the incorporation of resource assessment into computerized systems. The decision tree guides the development of pseudocode that can be incorporated into computer code.

## Slide 69: Pseudocode Example
For Each Land Cover At Site Remark: Develop list of potential resource concerns
and current conservation activities
For Each Use Objective
Add Use Objective RC [from Objective-Concern Table] to Potential RC List
Next
For Each Use Activity
Add Use Activity RC [from Activity-Concern Table] to Potential RC List
IF Use Activity is Conservation Activity THEN
Add Conservation Activity to Conservation Activity List
ENDIF
Next
For Each Built Feature
Add Built Feature RC [from Built Feature-Concern Table] to Potential RC List
IF Built Feature is Conservation Activity THEN
Add Built Feature to Conservation Built Feature List
ENDIF
Next
Next

## Slide 70: Generic Means to Address Resource Concerns
Use Limitation Concerns
  Accept the use limitation, i.e. limited achievement of site objectives
  Change site use and objectives to one not limited by the resource
  Improve resource use efficiency to meet objectives
  Improve onsite resource condition to meet objectives
  Obtain offsite resource to meet objectives
Hazard Concerns
  Avoid use of the hazardous area
  Prevent hazard condition from occurring
  Hazard-proof built land-use features
  Accept, insure, and remediate effects of hazard occurrence
Ecosystem Concerns
  Avoid ecosystem effects by ceasing or not undertaking a resource use, land use or land-use activity, or by not constructing a built feature
  Minimize ecosystem effects by limiting the intensity or extent of resource use, land use, or land-use activity, or from built features
  Prevent ecosystem affects from the land use through mechanisms to contain or trap these affects to the land use site

## Slide 71: To Be Continued…